December 2011.

The December 2011 seasonal forecast includes both 50% hydrology (D1641 and least restricted OMR flow) and 90% hydrology (D1641 and contingent).  The excel file includes EC and Bromide at Banks, Jones Pumping stations, Old River at Bacon Island, and Old River at Highway 4, and a few locations on the California Aqueduct.

This Seasonal forecast of Aqueduct water quality was based on:

- December 2011 DCO allocation study.

- Initial EC conditions in Aqueduct were established by the Delta and Aqueduct historical simulations up to the end of November, 2011.

- Bromide concentration at Jones and Banks PP was converted from modeled EC, bromide concentration in Aqueduct was modeled directly.

Both 50% and 90% hydrology studies were based on the following gate and temporary barriers operations:

- Delta Cross Channel  open during the following periods: June 1 to June 15, July 1 to Nov 26

- No physical HOR barrier is installed

- MR barrier is installed from April 15 to Nov 30

- OR barrier is installed from April 15 to Nov 30

- GLC barrier is installed from May 15 to Nov 30

*Notable points:

- Because the 50% hydrology has an “Above Normal” water year type, Fall X2 requirements are in effect for the 50% Moderate study for September, October and November.

| Net Delta Outflow Used for each Scenario (TAF) |  |
| --- | --- |
|  | 90% (Mod) | 90% (D1641) | 50% (Mod) | 50% (D1641) |
| Jan | 909 | 836 | 2086 | 2050 |
| Feb | 1010 | 972 | 3008 | 3101 |
| Mar | 1088 | 1108 | 2453 | 2501 |
| Apr | 602 | 602 | 1356 | 1067 |
| May | 473 | 473 | 959 | 753 |
| Jun | 423 | 423 | 705 | 514 |
| Jul | 311 | 307 | 496 | 492 |
| Aug | 290 | 286 | 372 | 368 |
| Sep | 249 | 245 | 410 | 267 |
| Oct | 257 | 257 | 424 | 257 |
| Nov | 268 | 268 | 411 | 268 |
| Dec | 307 | 307 | 323 | 308 |