The EXCEL file includes EC, Bromide at Banks, Jones Pumping stations, and locations on the California Aqueduct for the January 2011 allocation study for both 50% hydrology (D1641 and most restriction of OMR flow) and 90% hydrology (D1641 and most restriction of OMR flow).

This Seasonal forecast of Aqueduct water quality was based on:

- January 2011 DCO allocation study.

- Initial EC conditions in Aqueduct were established by the Delta and Aqueduct historical simulations up to the end of December, 2010.

- Bromide concentration at Jones and Banks PP was converted from modeled EC, bromide concentration in Aqueduct was modeled directly.

Both 50% and 90% hydrology studies were based on the following gate and temporary barriers operations.

- Delta Cross Channel  open during the following periods: May 1 to May 4, June 1 to June 15, July 1 to Nov 26

- No physical HOR barrier is installed

- MR barrier is installed from Apr 15 to Nov 30

- OR barrier is installed from Apr 15 to Nov 30

- GLC barrier is installed from May 15 to Nov 30